## Slide 1: 2022 427 Final Topics

## Slide 2: Chapters
Overview
Application layer
Transport layer
Network layer
Link layer
Network security

## Slide 3: Network Security
Plain text, ciphertext, encryption, description
Symmetric key crypto: DES/AES, features
public/private key crypto: RSA, features
Authentication: CA (public key certification authorities)
Digital signature
Hashing: MD5, SHA, features
Encrypting an email (confidentiality, integrity, authentication)
Notes: Symmetric = less computationally intensive, same and shared encrypt and decrypt key; challenge: how to share the key?
Asymmetric = public/private key; one key encrypts, and only the other can decrypt; can be used for digital signatures.
Need to get public key from CA to make sure you use the right (trusted) public key to decrypt a signed message by the sender who has the true private key.
Hashing: 1-way function; takes higher dimension data and compresses it to lower dimension (into fixed size; i.e. SHA 256 bits).

## Slide 4: Link Layer
Talking in a large room:
MAC protocol (who can talk）
  Channel (bandwidth) partitioning (TDMA) aka circuit switching, random access (try to transmit; if collision, do random backoff), taking turns (time paritioning)
  Random Access examples: Slotted aloha, CSMA/CD (binary backoff)
MAC Address （talk to whom)
Ethernet
Frame structure (source/dest MAC header; data; ECC trailer)
Switches:
  Collision domain
  Self-learning (ARP broadcasts)
  MAC addresses for sender & receiver

## Slide 5: Network layer
Forwarding: lookup the routing table (data plane)
IP protocol (IPv4)
IP Address:
  Subnet
  IP address shortage:
    Tunneling
    private/public (Network address translation)
How to lookup the routing table? Longest-prefix
Routing: build the routing table (control plane)
Link state (tell world… about … neighbors) step by step Dijkstra’s algorithm
Distance vector (tell neighbors … about world?)
Real life: autonomous system:
  BGP: iBGP, eBGP (uses distance vector protocol)
  OSPF (uses link state protocol)

## Slide 6: Transport layer
TCP/UDP segment structure, basic features，Port
Reliable data Transfer (TCP)
Basic elements:
  ACK
  Sequence numbers
  Timer
In practice (pipeline protocols):
  GBN (go back N)
  Selective repeat
TCP:
Sequence number, ACK
Connection establishment (3-step handshake), tear down (4 step termination)
Congestion control (prevent overwhelming receiver and hoggining the network)
  Slow start
  Congestion avoidance
Flow control
Flexible timeout

## Slide 7: Application layer
P2P vs. Client-server
P2P: self scalability (i.e., applications that rely on adHoc network infrastruture)
HTTP protocol (remember POST and GET requests and response code level)
Request line, status line
Request methods
Response codes
Persistent HTTP and non-persistent HTTP
DNS protocol
Hierarchical architecture
Iterated query vs. recursive query

## Slide 8: Overview
What is the Internet?
What is a protocol?
Internet structure?
Performance metrics: loss, delay (latency), bandwidth (physical characteristic; theoretically), throughput (actual bandwidth measured; always a fraction of theoretical bandwidth)
Protocol layers
Security

## Slide 9: What happens when you send an HTTP request?
THIS IS A VERY POPULAR QUESTION IF YOU TRULY UNDERSTAND COMPUTER NETWORKS. PROFESSOR SONG WAS ASKED THIS QUESTION TWICE WHEN HE APPLIED (2 DIFFERENT TIMES) FOR HIS PHD.
EXAM = TUESDAY DEC 13 @ 11:30AM TO 2:30PM. (ARRIVE AT 11AM TO BE SAFE!)